## Slide 1: U3_L3_ALL1
Class: 5 CM/TL Prof. Massimo Eccher
School year: 2017-18
NACA profiles

## Slide 2: NACA (National Advisory Committee for Aeronautics)
NACA, precursor to NASA, was a U.S. agency founded in 1915 to institutionalize aeronautical research.
The NACA airfoils are airfoil shapes described using a series of digits. Before NACA series, airfoil design was rather arbitrary.
The parameters in the code can be entered into equations to precisely generate the cross-section of the airfoil.
https://en.wikipedia.org/wiki/National_Advisory_Committee_for_Aeronautics#/media/File:NACA_seal.jpg

## Slide 3: NACA AIRFOIL NAMING CONVENTION
Early NACA series, 4- 5- digit series were generated with analytical equations.
Later families, including 6-digit series, are more complicated shapes.
camber mean line
chord
Leading edge radius
Example: 4-digit series
First digit specifies maximum camber in percentage of chord
Second digit indicates position of maximum camber in tenths of chord
Last two digits provide maximum thickness of airfoil in percentage of chord
By the author

## Slide 4: EXAMPLE: NACA FOUR-DIGIT SERIES
First digit specifies maximum camber in percentage of chord
Second digit indicates position of maximum camber in tenths of chord
Last two digits provide maximum thickness of airfoil in percentage of chord
Example: NACA 2415
Airfoil has maximum thickness of 15% of chord (0.15c)
Camber of 2% (0.02c) located 40% back from airfoil leading edge (0.4c)
Adapted from
https://commons.wikimedia.org/wiki/File:NACA_2415.svg

## Slide 5: AIRFOIL THICKNESS: World War I AIRPLANES
English Sopwith Camel
German Fokker Dr-1
Higher maximum CL
Higher rates of climb
Improved maneuverability
Lower maximum CL
Thin wing, bracing wires required
What about their NACA codes?
http://acepilots.com/wwi/sop_camel.html
http://www.fiddlersgreen.net/models/aircraft/Fokker-Dr1.html
https://riseofflight.com/forum/topic/26617-fokker-dvii/
https://riseofflight.com/forum/topic/26617-fokker-dvii/

## Slide 6: EXAMPLE: F-104 LOCKHEED STARFIGHTER
1958 – used in Vietnam
First airplane designed for sustained flight at Mach 2
Very sharp leading edge on wings (razor sharp leading edges, thickness 3.4 %)
Designed to minimize wave drag at supersonic speeds
Very poor low-speed aerodynamic performance
Such wings tend to stall at low angles of attack, CLmax is only about 1.15
Vstall (full) ~ 198 MPH, Vstall (empty) ~ 152 MPH (Vstall proportional to W1/2)
http://www.fiddlersgreen.net/models/
aircraft/Lockheed-F104.html

## Slide 7: EXAMPLE: BOEING 727
Commercial airplane
Designed in 1960’s to operate out of airports with relatively short runways
Desire to minimize take-off and landing distances
Maximum CL = 3.0
Vstall ~ 113 MPH
https://forum.ysfhq.com/viewtopic.php?t=4956
http://www.tailsthroughtime.com/2010/04/ive-always-had-soft-spot-for-boeing-727.html

## Slide 8
NACA 2415 flying right side up
Zero angle of attack
Lift in positive vertical direction
NACA 2415 upside down
Zero angle of attack
Lift in negative vertical direction
Positive angle of attack
Say =10º
Lift in positive vertical direction

What if we turn it upside down?
4 cases
Images adapted from:
http://www.apollocanard.com/4_airfoil%20design.htm

## Slide 9: CAN AN AIRFOIL PRODUCE LIFT WHEN IT IS FLYING UPSIDE DOWN?
NACA 2415 flying upside down at certain angles of attack will generate positive lift, but less than same airfoil right side up at the same angle of attack
Here is a way to understand this:
  If we take airfoil on left and turn it upside down it is same as airfoil right side up but with a negative angle of attack
  Therefore, lift coefficient for upside down airfoil at a positive angle of attack is given by data for negative angles of attack
  The negative cl connotes a downward lift on the ordinary right side up airfoil when pitched to a negative angle of attack
  In upside down orientation (airfoil on right), lift is directed upwards


Images adapted from:
http://www.apollocanard.com/4_airfoil%20design.htm